## Slide 1: A Program for Elsie, a 4-bit Computer
Or, Your Code Really Looks Like This

## Slide 2: What is a computer program?
It’s a set of computer instructions that accomplish a task

## Slide 3: Elsie is a tiny computer with a 4-bit bus

## Slide 4: Elsie can: Move a number from memory into the A register (where math can happen) Add a number to the A register Move the result back into memory

## Slide 5: Elsie, like all digital computers, only understands ones and zeros

## Slide 6: All our computers work very much like Elsie

## Slide 7: Writing a program for Elsie shows us what programs really look like and how they run.

## Slide 8: What does a program for Elsie look like?

## Slide 9: # this is a line comment # (first thing’s first!)

## Slide 10: # these are the only instructions # Elsie knows load # move data value into regA add # add data value to regA store # store contents of regA goto # this one we skip for now

## Slide 11: # this program adds 1 + 2 and # stores the result in # memory location 10 load 1 add 2 sto 10

## Slide 12: How does Elsie know what to do?

## Slide 13: When Elsie powers up, the hardware starts reading 4 binary bits (a nybble) at a time.

## Slide 14: Each instruction fits in one nybble.

## Slide 15: Elsie has an Instruction Pointer, a register that knows where the next instruction is.

## Slide 16: Let’s have a look at Elsie

## Slide 18: Back to the 4-bit nybbles Elsie’s been reading all this time

## Slide 19: Elsie’s hardware endlessly feeds the CPU 4-bit nybbles in pairs

## Slide 20: The first nybble is the instruction. The second nybble is data for that instruction to use.

## Slide 21: Elsie’s hardware: 1. fetches a 4-bit instruction nybble, 2. fetches a 4-bit data nybble, 3. executes the instruction with the data, and 4. repeats as long as power is on.

## Slide 22: On Elsie, each instruction has a 2-bit ID called an opcode: load = 00 add = 01 sto = 10 goto = 11

## Slide 23: Each 4-bit instruction nybble also contains a 2-bit mode that we skip for now
opcode | mode (always 00 for now)

## Slide 24: Back to our program..

## Slide 25: # this program adds 1 + 2 and # stores the result in # memory location 10 load 1 add 2 sto 10

## Slide 26: # this program is # much easier to read # with line comments! load 1 # put a 1 in register A add 2 # add 2 to register A sto 10 # store the result

## Slide 27: But Elsie only knows ones and zeros so we must translate

## Slide 28: We know the 2-bit opcode for each instruction, and

## Slide 29: We know the data for each instruction.

## Slide 30: To Elsie, our program looks like this load 1 0000 0001 add 2 0100 0010 sto 10 1000 1010

## Slide 31: (This translation to ones and zeros is what compilers do.)

## Slide 32: Elsie’s CPU is wired to execute each instruction.

## Slide 36: What do real computer instructions look like?

## Slide 37: A similar program in C++:

## Slide 38: Now the real computer instructions:

## Slide 39: Not too different from Elsie’s code, eh? load 1 0000 0001 add 2 0100 0010 sto 10 1000 1010